## Slide 1: Using the MPU with an RTOS to Enhance System Safety and Security
By
Stephen Ridley

## Slide 2
WITTENSTEIN high integrity systems: A World Leading RTOS Ecosystem

## Slide 3: Objectives
Safety Systems, Functional Safety, Software Components and Partitioning.
Multi Core and Multi Processor Architectures as a means of Partitioning.
Using the MPU to Partition and Protect.

## Slide 4: Safety, Security, Software and Systems
In embedded systems, when we talk about “Safety”, we usually mean ‘Functional Safety’. Every industry sector has its own set of standards setting out the development steps and verification activities required for a product to achieve a given Safety Integrity Level (SIL).
When we are talking about “Security”, we mean guaranteeing integrity, preventing intrusion and unauthorized use of resources.
For both of these aims, using an MPU can help by preventing code from operating or accessing data outside of its assigned bounds.
Does not matter which industry sector or standards we need to be compliant to, using an MPU can help to prove that the system is operating within its assigned parameters.
Finally, “Safety” and “Security” apply to “Systems” and can encompass multiple devices featuring hardware and software; however we are primarily concerned with software within this talk.

## Slide 5: Software Components and System Partitioning
Another use for an MPU is to enforce partitioning. This is just part of the wider subject of mixed SIL programming, where critical parts of the system are developed to the required SIL level. However, we may also use commercial grade software (COTS or SOUP) as well as lower grade software developed in house.
For full mixed SIL programming to work, we need to:
Identify safety functions and use case requirements.
Ensure that the system architecture can supply the necessary spatial separation (i.e. prohibit memory accesses by non-safety code that could compromise the operation of the safety software).
Ensure that the system architecture can supply the necessary temporal separation (i.e. prove that non-safety software cannot prevent the safety software having sufficient run time to achieve its purpose).
Be able to prove that the requirements have been correctly implemented.

## Slide 6: Use Case – An Embedded System
Standard practice says that all software must be developed to the highest SIL level required.
Control
Logic
Display
Driver
Output
Driver
Sensor
Processing
Flash
Driver
Flash Memory
Display
Actuator
S
S
S
S

## Slide 7: Use Case – An Embedded System
Control
Logic
Display
Driver
Output
Driver
Sensor
Processing
Flash
Driver
Flash Memory
Display
Actuator
S
S
S
S

## Slide 8: Use Case – Marketing and Ambitious Engineers Now Involved
Control
Logic
Display
Driver
Output
Driver
Sensor
Processing
Flash
Driver
Flash Memory
Display
Actuator
S
S
S
S
USB Device Stack
FAT File System
USB
SD Card
Network Stack
Ethernet

## Slide 9: Use Case – An Embedded System
We now have:
Critical safety software.
Commercial third party software that we have no control over.
Other software not developed to the required SIL.
Control
Logic
Display
Driver
Output
Driver
Sensor
Processing
Flash
Driver
Flash Memory
Display
Actuator
S
S
S
S
USB Device Stack
FAT File System
USB
SD Card
Network Stack
Ethernet

## Slide 10: Use Case – An Embedded System
For this system to be implementable in an acceptable manner for a safety system, we need to be able to demonstrate:
Spatial separation between the safety code/data and the non-safety code/data.
Temporal separation between the safety code and the non-safety code.
Data passed through non-safe components is either not safety related or protected by other protocols.
Control
Logic
Display
Driver
Output
Driver
Sensor
Processing
Flash
Driver
Flash Memory
Display
Actuator
S
S
S
S
USB Device Stack
FAT File System
USB
SD Card
Network Stack
Ethernet

## Slide 11: Using Multiple Processors to Achieve Separation
Relatively easy from a software perspective in that there is clear isolation between safety and non-safety components.
More expensive and complicated hardware (not optimal in low cost embedded systems).
Control
Logic
Display
Driver
Output
Driver
Sensor
Processing
Flash
Driver
Flash Memory
Display
Actuator
S
S
S
S
USB Device Stack
FAT File System
USB
SD Card
Network Stack
Ethernet
Control
Logic
Safety Processor
Support Processor

## Slide 12: Using a Multi-Core Processor to Achieve Separation
Easier hardware design, only one set of peripheral components.
As both cores typically share access to memory and peripherals it is difficult to claim spatial separation without using an MMU or MPU.
Control
Logic
Display
Driver
Output
Driver
Sensor
Processing
Flash
Driver
Flash Memory
Display
Actuator
S
S
S
S
USB Device Stack
FAT File System
USB
SD Card
Network Stack
Ethernet
Control
Logic
Safety Core
Support Core
RAM
Flash Memory
Shared Peripherals

## Slide 13: A Single Core System has no Inherent Separation.
Different approach needed to achieve spatial separation.
An MPU or MMU can be used to achieve spatial separation.
Control
Logic
Display
Driver
Output
Driver
Sensor
Processing
Flash
Driver
Flash Memory
Display
Actuator
S
S
S
S
USB Device Stack
FAT File System
USB
SD Card
Network Stack
Ethernet
Control
Logic
Single Core
Hardware Peripherals
RAM
Flash Memory

## Slide 14: Using a Memory Protection Unit (MPU)
The MPU is used to prevent access to unauthorised regions within the memory map.
Microprocessors that have an MPU typically allow a number of “memory regions” to be defined. This is usually a memory range and associated access permissions.
Some differences depending on the silicon manufacturer (e.g. ARC processors feature prioritised MPU regions whereas others are additive with respect to granting of permissions).
Whatever the flavour, the action is the same, a processor exception will be generated if an illegal access is attempted.
RAM
FLASH
Region 1 (RW)
Region 0 (RX)
Any access will generate a fault.
OK to read or write, but a jump
will generate an access fault.
Region 2 (RW)
Region 3 (RW)
ADC
SPI
Access permitted to ADC and SPI peripherals only.

## Slide 15: Using a Memory Protection Unit (MPU)
Use processor privilege modes. Different access permissions can be granted depending on whether the processor is running in privileged mode or not.
Region 4 (Sup RX + User RX)
Region 6 (Sup RW + User NA)
Region 7 (Sup RX + User NA)
Privileged (Safety) RAM
UART
Privileged (Safety) Code
Unprivileged Code
General Access RAM
Region 5 (Sup RW + User NA)
Region 3 (Sup RW + User RW)
Region 2 (Sup RW + User RW)

## Slide 16: MPU and a Real Time Operating System (RTOS)
When using an RTOS, the application is broken up into tasks or threads. Communication between tasks is frequently accomplished with Queues or Events that are managed by the RTOS.
This gives much more opportunity for enforcing partitioning at a fundamental level if the RTOS provides native support for the MPU.
If the RTOS in use does not provide native support for the MPU, then we have a similar scenario to the previous arrangements except that we have a new problem, the code and data for the RTOS itself. This has to be trusted at the highest SIL level of the application.
Region 4 (Sup RX + User RX)
Region 6 (Sup RW + User NA)
Region 7 (Sup RX + User NA)
Privileged (Safety) RAM
UART
Privileged (Safety) Code
Unprivileged Code
General Access RAM
Region 5 (Sup RW + User NA)
Region 3 (Sup RW + User RW)
Region 2 (Sup RW + User RW)
RTOS Code and Data

## Slide 17: Using an RTOS with Integrated MPU Support (e.g. SAFERTOS)
Integrated MPU Support allows us to:
Protect the RTOS Kernel Code and Data from unauthorised access using fixed regions that are setup during system initialisation.
Peripherals
Region 7 (Sup RX + User RX)
Region 0 (Sup RW + User NA)
Region 1 (Sup RX + User NA)
Kernel Data
Kernel Code
Application Code
Application RAM
Region 6 (Sup RW + User RW)
Note: This example assumes 8 prioritised MPU regions where low number regions are high priority.

## Slide 18: Using an RTOS with Integrated MPU Support
Integrated MPU Support allows us to:
Provide a degree of task isolation by protecting user task stacks. Some MPU regions are reprogrammed on each context switch.
Region 7 (Sup RX + User RX)
Region 0 (Sup RW + User NA)
Region 1 (Sup RX + User NA)
Peripherals
Kernel Data
Kernel Code
Application Code
Region 6 (Sup RW + User RW)
Peripherals
Kernel Data
Kernel Code
Application Code
Peripherals
Kernel Data
Kernel Code
Application Code
Region 2 (Sup RW + User RW)
Region 2 (Sup RW + User RW)
Region 2 (Sup RW + User RW)
TASK 1
TASK 2
TASK 3

## Slide 19: Using an RTOS with Integrated MPU Support
Integrated MPU Support allows us to:
Reprogram the MPU during each context switch and therefore allow each task to have its own set of configurable regions.
Region 7 (Sup RX + User RX)
Region 0 (Sup RW + User NA)
Region 1 (Sup RX + User NA)
Peripherals
Kernel Data
Kernel Code
Application Code
Region 6 (Sup RW + User RW)
Peripherals
Kernel Data
Kernel Code
Application Code
Peripherals
Kernel Data
Kernel Code
Application Code
Region 2 (Sup RW + User RW)
Region 2 (Sup RW + User RW)
Region 2 (Sup RW + User RW)
TASK 1
TASK 2
TASK 3
Global data region.
Region 5 (Sup RW +
User RW)
Global data region.
Region 5 (Sup RW +
User RO)
Shared data region.
Region 3
User RW
User RO
Private data
region
Notes: Colours show different memory regions – global data in red with different access permissions.
Blue is a region shared between tasks 1 and 2
Orange is private to task 3.

## Slide 20: Common Problems with Using the MPU
Human nature – designing the memory map, managing the linker script etc. are non trivial especially when the development spans multiple teams. The tendency to allocate everything to shared data or declare the task privileged has to be managed.
Not enough regions – even when everybody is on-board, most microprocessors do not offer enough memory regions to really control the memory space.
Interrupt handlers – will always be privileged and therefore typically are not constrained by the MPU. Or if they are constrained then they will run with permissions in force when the exception occurs.
What to do when an error is detected – in a microprocessor based system, managing to recover from a major fault condition such as a hard fault or MPU fault is difficult.

## Slide 21: Summary
Why an MPU can be helpful in systems that need to be certified as safe or secure.
Multi Core and Multi Processor Architectures as a means of partitioning and how the MPU is still useful.
What we can do with the MPU to partition and protect.
How an RTOS that natively supports the MPU gives greater scope with regards to partitioning.